## Slide 1: SEG i8243 UFP Project Trainee: Antara Rahman Project Start/ End date: August 9th,2024 to September 4th,2024 Mentor: Jordan Cantillano

## Slide 2: Agenda
Project Overview
Test Block Introduction
Test Overview and Results – Data log
Test Program Results – Test Time Analysis
Test Program Results – Repeatability
Challenges
Project Schedule – Excepted vs. Actual
Skill Assessment – Before vs. After
Effectiveness of Project
Thank you!
Q&A
Notes: 40 mins-1hr

## Slide 3: Project Overview
Background Knowledge:
  I8243 Model Device: Used as the first mini project in IGXL family digital programming basic training.
  FPGA Training Kit: Can be set to I8243 mode to simulate the device’s function.
  Alternative Setup: Allows users to complete the I8243 mini project without standard lab hardware.
  Configuration Requirement: Training kit hardware must be connected to a configuration server and configured via the GUI to I8243 mode.
Feature and Description:
  Intel I8243 Device: An input/output expander for the MCS-48 family of single-chip microcomputers.
  I/O Ports: Four 4-bit bidirectional static I/O ports interfacing with MCS-48 microcomputers.
  Efficient I/O Expansion: Uses only 4 I/O lines of the 8048 for expansion, allowing multiple 8243s on the same bus.
  Direct Extension: I/O ports serve as a direct extension of the MCS-48 microcomputers’ resident I/O facilities.
  Instruction Access: Accessed by MOV, ANL, and ORL instructions.

## Slide 4: Test Block Introduction
Power-On Initialization: Initial application of power forces I/O pins 4, 5, 6, & 7 to tri-state and port 2 to input mode. The first high-to-low transition of the PROG pin exits the power-on mode. The power-on sequence is re-initiated if VCC drops below 1.65V/VCCIO drops below 3V.
Write Modes: The device supports three write modes: MOVD,ORLD and ANLD. To write to an output port, we program the Operation code (op-code) and the port address to port 2 during high-to-low transitions on CS and PROG. Data is transferred to the logic block of the specified output port.
Read Mode: The device has one read mode. we program the Operation code (op-code) and the port address to port 2 during high-to-low transitions on CS and PROG. The selected port (4, 5, 6, 7) switches to tri-state mode, and port 2 returns to input mode.
Power Requirements: The simulated Intel 8243 requires two power supplies: VCC = 1.8V and VCCIO = 3.3V.
Timing Performance: The timing performance of the simulated Intel 8243 is deciphered from the datasheet waveform as seen in Figure 2. The I/O port 2 is used to send instructions and write data when PROG and CS pins are transitioning. The output is compared at ports 4-7 based on the data written in port 2.
Notes: -Power Requirements: This device uses LVCMOS33 logic levels (0 to 3.3V).
-From these, ORLD(ORs new data with old data and writes the result to the selected port.) and ANLD(ANDs new data with old data and writes the result to the selected port.
-Normally, a port will be in output (write mode) or input (read mode).If modes are changed during operation, the first read following a write should be ignored to allow the external driver to settle.A read of any port will leave that port in a high impedance state.

## Slide 5: Test Overview and Results – Data log Continuity Tests Three Continuity tests are performed: 1. Shorts Test Using Dynamic Loads 2.Open Test Using Dynamic Loads 3. Parametric Continuity Test
Process
(Open and Short Test)
Process
(Parametric Continuity Test)
Notes: -Power Requirements: This device uses LVCMOS33 logic levels (0 to 3.3V).
-From these, ORLD(ORs new data with old data and writes the result to the selected port.) and ANLD(ANDs new data with old data and writes the result to the selected port.
-Normally, a port will be in output (write mode) or input (read mode).If modes are changed during operation, the first read following a write should be ignored to allow the external driver to settle.A read of any port will leave that port in a high impedance state.

## Slide 6: Test Overview and Results – Data log Continuity Tests
Results
(Open and Short Test)
Results
(Parametric Continuity Test)
Notes: -Power Requirements: This device uses LVCMOS33 logic levels (0 to 3.3V).
-From these, ORLD(ORs new data with old data and writes the result to the selected port.) and ANLD(ANDs new data with old data and writes the result to the selected port.
-Normally, a port will be in output (write mode) or input (read mode).If modes are changed during operation, the first read following a write should be ignored to allow the external driver to settle.A read of any port will leave that port in a high impedance state.

## Slide 7: Test Overview and Results – Data log Leakage Tests Two leakage tests are performed: 1. Input Leakage 2. Output tristate leakage
Process
(Input Leakage)
Process
(Output tristate leakage)
Notes: -Power Requirements: This device uses LVCMOS33 logic levels (0 to 3.3V).
-From these, ORLD(ORs new data with old data and writes the result to the selected port.) and ANLD(ANDs new data with old data and writes the result to the selected port.
-Normally, a port will be in output (write mode) or input (read mode).If modes are changed during operation, the first read following a write should be ignored to allow the external driver to settle.A read of any port will leave that port in a high impedance state.

## Slide 8: Test Overview and Results – Data log Leakage Tests
Results
(Input Leakage)
Results
(Output tristate leakage)
Notes: -Power Requirements: This device uses LVCMOS33 logic levels (0 to 3.3V).
-From these, ORLD(ORs new data with old data and writes the result to the selected port.) and ANLD(ANDs new data with old data and writes the result to the selected port.
-Normally, a port will be in output (write mode) or input (read mode).If modes are changed during operation, the first read following a write should be ignored to allow the external driver to settle.A read of any port will leave that port in a high impedance state.

## Slide 9: Test Overview and Results – Data log Functional Test The functional test has 3 main steps: -use write instruction for 1010 on port 4-7 -use AND instruction for port 4-7 so I get 1110 AND existing data -use OR instruction for port 4-7 so I get 0011 OR existing data
Process
(Pattern Tool)
Process
(Time Set)
Notes: -Power Requirements: This device uses LVCMOS33 logic levels (0 to 3.3V).
-From these, ORLD(ORs new data with old data and writes the result to the selected port.) and ANLD(ANDs new data with old data and writes the result to the selected port.
-Normally, a port will be in output (write mode) or input (read mode).If modes are changed during operation, the first read following a write should be ignored to allow the external driver to settle.A read of any port will leave that port in a high impedance state.

## Slide 10: Test Overview and Results – Data log Functional Test
Results
(Waveform)
Results
(Datalog)
Notes: -Power Requirements: This device uses LVCMOS33 logic levels (0 to 3.3V).
-From these, ORLD(ORs new data with old data and writes the result to the selected port.) and ANLD(ANDs new data with old data and writes the result to the selected port.
-Normally, a port will be in output (write mode) or input (read mode).If modes are changed during operation, the first read following a write should be ignored to allow the external driver to settle.A read of any port will leave that port in a high impedance state.

## Slide 11: Test Overview and Results – Data log ICC Tests Two ICC tests are performed: 1. Static ICC 2. Dynamic ICC
Process
(Static ICC)
Process
(Dynamic ICC)
Notes: -Power Requirements: This device uses LVCMOS33 logic levels (0 to 3.3V).
-From these, ORLD(ORs new data with old data and writes the result to the selected port.) and ANLD(ANDs new data with old data and writes the result to the selected port.
-Normally, a port will be in output (write mode) or input (read mode).If modes are changed during operation, the first read following a write should be ignored to allow the external driver to settle.A read of any port will leave that port in a high impedance state.

## Slide 12: Test Overview and Results – Data log ICC Tests
Results
(Static ICC)
Results
(Dynamic ICC)
Notes: -Power Requirements: This device uses LVCMOS33 logic levels (0 to 3.3V).
-From these, ORLD(ORs new data with old data and writes the result to the selected port.) and ANLD(ANDs new data with old data and writes the result to the selected port.
-Normally, a port will be in output (write mode) or input (read mode).If modes are changed during operation, the first read following a write should be ignored to allow the external driver to settle.A read of any port will leave that port in a high impedance state.

## Slide 13: Test Overview and Results – Data log Rise/Fall time Tests Using a pattern and Characterization studio, the following tests are performed: 1. Rise Time Test 2. Fall Time Test
Process
(Rise Time)
Process
(Fall Time)
Notes: -Power Requirements: This device uses LVCMOS33 logic levels (0 to 3.3V).
-From these, ORLD(ORs new data with old data and writes the result to the selected port.) and ANLD(ANDs new data with old data and writes the result to the selected port.
-Normally, a port will be in output (write mode) or input (read mode).If modes are changed during operation, the first read following a write should be ignored to allow the external driver to settle.A read of any port will leave that port in a high impedance state.

## Slide 14: Test Overview and Results – Data log Rise/Fall time Tests
Results
(Rise Time)
Results
(Fall Time)
Notes: -Power Requirements: This device uses LVCMOS33 logic levels (0 to 3.3V).
-From these, ORLD(ORs new data with old data and writes the result to the selected port.) and ANLD(ANDs new data with old data and writes the result to the selected port.
-Normally, a port will be in output (write mode) or input (read mode).If modes are changed during operation, the first read following a write should be ignored to allow the external driver to settle.A read of any port will leave that port in a high impedance state.

## Slide 15: Test Program Results – Test Time Analysis
Original test time
Latest test time and what I did to get there
Notes: -Power Requirements: This device uses LVCMOS33 logic levels (0 to 3.3V).
-From these, ORLD(ORs new data with old data and writes the result to the selected port.) and ANLD(ANDs new data with old data and writes the result to the selected port.
-Normally, a port will be in output (write mode) or input (read mode).If modes are changed during operation, the first read following a write should be ignored to allow the external driver to settle.A read of any port will leave that port in a high impedance state.

## Slide 16: Test Program Results – Repeatability
Running 50 loops and using the stdf file for analysis in galaxy
Show pareto and passing results here
Discuss cpk issue for fall time test, potentially compare previous errors and the latest error to show progress
Notes: -Power Requirements: This device uses LVCMOS33 logic levels (0 to 3.3V).
-From these, ORLD(ORs new data with old data and writes the result to the selected port.) and ANLD(ANDs new data with old data and writes the result to the selected port.
-Normally, a port will be in output (write mode) or input (read mode).If modes are changed during operation, the first read following a write should be ignored to allow the external driver to settle.A read of any port will leave that port in a high impedance state.

## Slide 17: Project Challenges
Test plan setup and understanding what level and how it affects your test program
Based on Tests, output leakage and functional test challenges, characterization studio challenges
Repeatability issue derived from cpk for fall time (spikes and how you overcame that)
What helped
Notes: -Power Requirements: This device uses LVCMOS33 logic levels (0 to 3.3V).
-From these, ORLD(ORs new data with old data and writes the result to the selected port.) and ANLD(ANDs new data with old data and writes the result to the selected port.
-Normally, a port will be in output (write mode) or input (read mode).If modes are changed during operation, the first read following a write should be ignored to allow the external driver to settle.A read of any port will leave that port in a high impedance state.

## Slide 18: Project Schedule – Excepted vs. Actual
Gantt Chart Comparison
Notes: -Power Requirements: This device uses LVCMOS33 logic levels (0 to 3.3V).
-From these, ORLD(ORs new data with old data and writes the result to the selected port.) and ANLD(ANDs new data with old data and writes the result to the selected port.
-Normally, a port will be in output (write mode) or input (read mode).If modes are changed during operation, the first read following a write should be ignored to allow the external driver to settle.A read of any port will leave that port in a high impedance state.

## Slide 19: Skill Assessment – Before vs. After Test Concept
The purpose of each test, as well as its corresponding pin levels, limits and binning are rated between 1(Very Low) and 5(Very High)
Items | Before |  |  |  |  | After |  |  |  | 
Test Concept | Do not have any knowledge on the particular topic |  | Have good knowledge of the topic but is not sure of how to apply in practice |  | Have good understanding of the topic and knows how to apply in practice | Do not have any knowledge on the particular topic |  | Have good knowledge of the topic but is not sure of how to apply in practice |  | Have good understanding of the topic and knows how to apply in practice
 | 1 | 2 | 3 | 4 | 5 | 1 | 2 | 3 | 4 | 5
Understanding of Device Data Sheets |  |  |  | √ |  |  |  |  |  | √
Translating from Data Sheets to Test Plans |  |  |  |  |  |  |  |  |  | 
Includes :- |  |  |  |  |  |  |  |  |  | 
Tests to be performed |  |  | √ |  |  |  |  | √ |  | 
Test Specifications |  |  | √ |  |  |  |  |  | √ | 
Instrument setups |  |  | √ |  |  |  |  | √ |  | 
Test Limits |  |  | √ |  |  |  |  |  | √ | 
Test Binning |  | √ |  |  |  |  |  |  | √ | 
Understanding Timing Diagrams |  | √ |  |  |  |  |  |  |  | √
Specifying Pin Levels |  | √ |  |  |  |  |  |  |  | √
Continuity Test |  |  |  | √ |  |  |  |  |  | √
Functional Test |  | √ |  |  |  |  |  |  |  | √
Supply Current ICC Test |  | √ |  |  |  |  |  |  | √ | 
Leakage Test | √ |  |  |  |  |  |  |  |  | √
Functional Test | √ |  |  |  |  |  |  |  |  | √
Rise/ Fall Time Test |  |  |  | √ |  |  |  |  |  | √
Conclusions: Significantly improved understanding of timing diagrams and how to apply waveform information in datasheets to functional test. Also improved understanding of the purpose of each tests and setup methods.
Notes: -Power Requirements: This device uses LVCMOS33 logic levels (0 to 3.3V).
-From these, ORLD(ORs new data with old data and writes the result to the selected port.) and ANLD(ANDs new data with old data and writes the result to the selected port.
-Normally, a port will be in output (write mode) or input (read mode).If modes are changed during operation, the first read following a write should be ignored to allow the external driver to settle.A read of any port will leave that port in a high impedance state.

## Slide 20: Skill Assessment – Before vs. After Software Programming
The set up of each test, understanding of the program structure and use of IG-XL functions are rated between 1(Very Low) and 5(Very High)
Items | Before |  |  |  |  | After |  |  |  | 
Software Programming | Do not have any knowledge on the particular item |  | Have good knowledge of the particular item but is not sure of how to apply in practice |  | Have good understanding of the particular item and knows how to apply in practice | Do not have any knowledge on the particular item |  | Have good knowledge of the particular item but is not sure of how to apply in practice |  | Have good understanding of the particular item and knows how to apply in practice
Test Program Development | 1 | 2 | 3 | 4 | 5 | 1 | 2 | 3 | 4 | 5
Test List: |  |  |  |  |  |  |  |  |  | 
Continuity using Dynamic Loads |  | √ |  |  |  |  |  |  |  | √
Parametric Continuity Test |  |  | √ |  |  |  |  |  |  | √
Static ICC Test |  |  | √ |  |  |  |  |  | √ | 
Dynamic ICC Test |  |  | √ |  |  |  |  |  | √ | 
IIL Leakage Test |  | √ |  |  |  |  |  |  |  | √
IOZ Leakage Test |  | √ |  |  |  |  |  |  |  | √
Functional Test |  | √ |  |  |  |  |  |  |  | √
Rise/ Fall Time Test |  |  | √ |  |  |  |  |  | √ | 
Program Structure: |  |  |  |  |  |  |  |  |  | 
Site-Aware Environment | √ |  |  |  |  | √ |  |  |  | 
Error Handling |  | √ |  |  |  |  | √ |  |  | 
IG-XL Functions: |  |  |  |  |  |  |  |  |  | 
IG-XL Help |  | √ |  |  |  |  |  |  | √ | 
IG-XL Pinlistdata Object | √ |  |  |  |  | √ |  |  |  | 
Conclusions: Significantly improved understanding of all test program set ups, as well as how to create patterns and time set sheets from scratch. Also successfully utilized IG-XL help and MyInfo for guidance on test program setup.
Notes: -Power Requirements: This device uses LVCMOS33 logic levels (0 to 3.3V).
-From these, ORLD(ORs new data with old data and writes the result to the selected port.) and ANLD(ANDs new data with old data and writes the result to the selected port.
-Normally, a port will be in output (write mode) or input (read mode).If modes are changed during operation, the first read following a write should be ignored to allow the external driver to settle.A read of any port will leave that port in a high impedance state.

## Slide 21: Skill Assessment – Before vs. After Test Debugging
Debugging skills using various IG-XL instruments are rated between 1(Very Low) and 5(Very High)
Items | Before |  |  |  |  | After |  |  |  | 
Test Debugging | Do not have any knowledge on the particular item |  | Have good knowledge of the particular item but is not sure of how to apply in practice |  | Have good understanding of the particular item and knows how to apply in practice | Do not have any knowledge on the particular item |  | Have good knowledge of the particular item but is not sure of how to apply in practice |  | Have good understanding of the particular item and knows how to apply in practice
Test Program Debugging |  |  |  |  |  |  |  |  |  | 
Basic Debug |  |  |  |  |  |  |  |  |  | 
Ability to set and run to trap |  |  | √ |  |  |  |  |  |  | √
Ability to debug using debug tool |  | √ |  |  |  |  |  |  |  | √
Continuity |  |  |  |  |  |  |  |  |  | 
Ability to debug using PPMU |  | √ |  |  |  |  |  |  | √ | 
DCVI Debug |  |  |  |  |  |  |  |  |  | 
Ability to debug using DCVI |  | √ |  |  |  |  | √ |  |  | 
Characterization |  |  |  |  |  |  |  |  |  | 
Ability to obtain Vil, Vih, Vol, Voh, Iol, Ioh from Characterization |  | √ |  |  |  |  |  |  | √ | 
Digital Debug |  |  |  |  |  |  |  |  |  | 
Ability to debug using Pattern tool | √ |  |  |  |  |  |  |  |  | √
Ability to debug using HRAM Display |  | √ |  |  |  |  | √ |  |  | 
Plot Actual Device Waveform using Waveform Display | √ |  |  |  |  |  |  |  |  | √
Conclusions: Much more accustomed to IG-XL instruments for debugging compared to before the project. Learned how to use Debug tool and step through programs, Waveform display to assess functional test failures, and finally, the characterization studio for rise and fall time tests.
Notes: -Power Requirements: This device uses LVCMOS33 logic levels (0 to 3.3V).
-From these, ORLD(ORs new data with old data and writes the result to the selected port.) and ANLD(ANDs new data with old data and writes the result to the selected port.
-Normally, a port will be in output (write mode) or input (read mode).If modes are changed during operation, the first read following a write should be ignored to allow the external driver to settle.A read of any port will leave that port in a high impedance state.

## Slide 22: Effectiveness of Project
Gave context into the labs that were done
Questioned things I otherwise did not think about and therefore learned more about utilizing IGXL and corresponding tools
Better idea of how to debug through problems
What each test does and a baseline of how to set them up
Notes: -Power Requirements: This device uses LVCMOS33 logic levels (0 to 3.3V).
-From these, ORLD(ORs new data with old data and writes the result to the selected port.) and ANLD(ANDs new data with old data and writes the result to the selected port.
-Normally, a port will be in output (write mode) or input (read mode).If modes are changed during operation, the first read following a write should be ignored to allow the external driver to settle.A read of any port will leave that port in a high impedance state.

## Slide 23: Thank you!
Mentor
Instructors
1-1 engineers
Notes: -Power Requirements: This device uses LVCMOS33 logic levels (0 to 3.3V).
-From these, ORLD(ORs new data with old data and writes the result to the selected port.) and ANLD(ANDs new data with old data and writes the result to the selected port.
-Normally, a port will be in output (write mode) or input (read mode).If modes are changed during operation, the first read following a write should be ignored to allow the external driver to settle.A read of any port will leave that port in a high impedance state.

## Slide 24: Q&A
Notes: -Power Requirements: This device uses LVCMOS33 logic levels (0 to 3.3V).
-From these, ORLD(ORs new data with old data and writes the result to the selected port.) and ANLD(ANDs new data with old data and writes the result to the selected port.
-Normally, a port will be in output (write mode) or input (read mode).If modes are changed during operation, the first read following a write should be ignored to allow the external driver to settle.A read of any port will leave that port in a high impedance state.

## Slide 25
Appendix
  Datasheet stuff that may be important
  Waveforms not in presentation
  Test instances
  Flow Table